Tarkistuslista C172/TAE125 OH-CAU
before engine start
preflight inspection	complete
seats and belts	checked
fuel selector valve	set
avionics master switch	off
electrical switches	off
parking brake	set
circuit breakers	in
alternate air door	closed
batt, alt, main switches	on
thrust lever	free movement
load display	0% rpm
rotating beacon	on
electrical fuel pump	on
thrust lever	idle
propeller	clear
ignition switch	on
glow light	off

Ready for Engine Start

after engine start
ced test button	press
oil pressure	check
ammeter	check
avionics master switch	on
electric fuel pump	off
radios	on
engine warm up	oil temp 50ºC
coolant temp 60ºC
2 minutes 890 RPM, then 1400 RPM
taxi
lights	as required
brakes	test
controls	free
flight instruments	check
flaps	0º or 10º
before takeoff
brakes	set
cabin doors and windows	closed
fuel selector valve	set
trim	set
FADEC AND PROP FUNCTION CHECK:
thrust lever	idle
fadec	test
thrust lever	full forward
load display min 94% — RPM 2240-2300
thrust lever	idle
engine instruments & ammeter	check
suction gauge	check
electrical fuel pump	on
radios	set
navigation aids	set
takeoff briefing	performed
pitot heat	as required
lights	as required
brakes	release
normal takeoff
directional gyro	set
thrust lever	full power
rotation	55 KIAS
climb speed	Vy 69 KIAS
Vx 62 KIAS
altitude 300 ft	flaps up
electric fuel pump	off
landing light	off
APPROACH CHECK
seats and belts	checked
fuel selector valve	set
electric fuel pump	on
landing light	as required
airspeed	69-80 KIAS
airspeed in final app	flaps 20º: 63 KIAS
flaps 40º: 60 KIAS
after landing
flaps	up
electrical fuel pump	off
transponder	stby
parking
parking brake	set
thrust lever	idle
avionics master switch	off
electric equipment	off
alternator and main switches	off
ignition switch	off
battery switch	off
control lock	install

MALMI TWR	131.25
MALMI GND	121.60
MALMI ATIS	122.70
HELSINKI APP	119.10
HELSINKI TWR	118.60

OH-CAU SPEEDS
rotation speed	55 KIAS
climb speed	70-85 KIAS

best angle of climb Vx	62 KIAS
best rate of climb Vy	69 KIAS

flap speed 10º	< 110 KIAS
flap speed 10-40º	< 85 KIAS

window open speed	160 KIAS

Max dem crosswind comp	17 KTS

temperatures (jet a-1)
min fuel temp before t/o	-30ºC
min fuel temp during flight	-36ºC

engine oil
level min	4.5 L
level max	6.0 L